#### Modello: CH-2/R13D

| Engine |  |
| --- | --- |
| Engine model | Kubota Z-482 |
| Max Power (3600 rpm) | Hp / Kw 13 / 9.6 |
| Cooling | Water |
| Start | Electric |
| Battery | 12V – 44Ah |
| Displacement | 479 cm3 |
| Cylinders | 2 |
| Max Torque | 3.00 daNm - 2600 rpm |
| Operational weight |  |
| Under carriage | 485 Kg |
| CH-2/R/CA alluminium platform | 555 Kg |
| CH-2/R/C-CP body with front door | 570 / 645 Kg |
| CH-2/R/MT-MTP dumping skip | 580 / 650 Kg |
| CH-2/R/AV-AVP high tip skip | 690 / 775 Kg |
| CH-2/R/BET mixer | 730 Kg |
| CH-2/R/ESC hydraulic backhoe | 775 Kg |
| Operational loading |  |
| All versions | 500 Kg |
| CH-2/R/AV-AVP | 450 Kg |
| Road transportable load |  |
| All versions | 800 Kg |
| Features |  |
| Transmission | Hydrostatic |
| Transmission pumps with variable cubic capacity | n° 2 |
| Total delivery | 27.7 lt/min |
| Gear pump flow | 6.8 lt/min |
| Max working pressure utilities | 150 bar |
| Max speed | 4.2 Km/h |
| Rubber track tensioning: adjustable screw + spring | • |
| Steering through indipendent tracks and negative brakes | • |
| Track width | 180 mm |
| Max gradient capability with operational loading | 30.00% |
| Refuelling |  |
| Fuel tank capacity | 10 lt |
| Hydraulic oil tank capacity | 20 lt |

#### Dumper MESSERSI  CH-2/R13D